Planning Department,

Planning Commission; Councilors Mason, Dober, Bushor: Ordinance Committee

# Twelve

COMPREHENSIVE DEVELOPMENT ORDINANCE—

Neighborhood Mixed Use Districts

ZA 12-06

That Appendix A, Comprehensive Development Ordinance, of the Code of Ordinances of the City of Burlington be and hereby is amended by amending Sections 4.4.2 (Neighborhood Mixed Use Districts) and Table 4.4.2-1 (Dimensional Standards and Density) thereof to read as follows:

### Sec. 4.4.2	Neighborhood Mixed Use Districts

(a)        Purpose:  As written

(b)	Dimensional Standards and Density:

The density and intensity of development, dimensions of building lots, the heights of buildings and their setbacks from property boundary lines, and the limits on lot coverage shall be governed by the following standards:

| Table 4.4.2 -1 Dimensional Standards and Density |
| --- |
| Districts | Max. Intensity (floor area ratio1) | Max. Lot Coverage | Minimum Building Setbacks (feet) Front4 Side2 Rear2 | Height (feet) |
| NAC | 2.0 FAR | 80%5 | 0 | 0 | 0 | Max: 35 |
| NMU | 2.0 FAR | 80% | 06 | 0 | 04 | Min: 203 Max: 35 |
| NAC-Riverside | 2.0 FAR | 80% | 0 | 0 | 0 | Min: 203 Max: 35 |
| Floor area ratio is defined in Art. 13 and described in Art 5. Actual maximum build out potential may be reduced by site plan and architectural design considerations of Art 6. Structures shall be setback a minimum of 15-feet along any property line that abuts a residential zoning district. Minimum building height shall be 20-feet and 2 stories. Measurement of and exceptions to height standards are found in Art 5. Bonuses for additional building height are described in section (d)2 below. All structures shall be setback 12-feet from the curb on a public street. Exceptions to minimum lot coverage are provided in (d)1. Not withstanding footnote 4, the NMU district at the intersection of Pine St. and Flynn Avenue shall have a minimum front yard setback of 10 feet. |

2

COMPREHENSIVE DEVELOPMENT ORDINANCE—

Neighborhood Mixed Use Districts

ZA 12-06

#### (c)	Permitted and Conditional Uses:  As written

#### (d)	District Specific Regulations:

##### 1.	Ground Floor Residential Uses Restricted

In order to maintain an active streetscape for pedestrians and pedestrian-oriented businesses and activities, residential uses shall not be permitted along the street-level frontage of any structure in the NAC District.

##### 2.	Exception to Maximum Lot Coverage in NAC District  As written, re-numbered.

*	Material stricken out deleted.

**	Material underlined added.

lb/emb/c: Ordinances 2012/Zoning Amendment ZA 12-06 re NAC Minimum Building Height, Sec. 4.4.2, Table 4.4.2-1

3/19/12; 5/25/12