Councilor Ashe,

CEDO, Code Enforcement, Ordinance Com.

# Eight

HOUSING -

Minimum Housing Amendments related to Lead Paint

That Chapter 18, Housing, of the Code of Ordinances of the City of Burlington be and hereby is amended by amending Sections 18-2, 18-25, 18-72 and adding 18-112 thereof to read as follows:

Sec. 18-2.  Definitions.

For the purposes of this chapter, the following terms, phrases, words, and their derivations, shall have the meanings given herein:

**********

Certified lead inspector means a person who has been licensed by the Vermont Department of Health to conduct lead inspections.

EMP shall mean essential maintenance practices required by section 1759 of title 17 of the Vermont Statutes Annotated.

Pre-Renovation Rule means the EPA 406b Rule, or any subsequent superseding rule that is in effect and applicable, that relates to renovations performed in pre-1978 housing which are performed for compensation.  For purposes of this definition, “renovation” means any modification of all or part of any existing structure in the housing that disturbs painted surfaces. “Renovation” includes : removal or modification of painted surfaces, components, or structures, surface preparation activities (i.e. sanding/scraping/other activities that may create paint dust) or window replacement. “Compensation” is the receipt of anything of value and may include exchanges of money, goods, or services or the payment of rent to landlords or property managers.

Rental target housing means target housing offered for lease or rental under a rental agreement as defined in 9 V.S.A. § 4451. "Rental target housing" does not include a rented single room located within a dwelling in which the owner of the dwelling resides unless a child six years of age or younger resides in or is expected to reside in that dwelling.

Target housing means any dwelling constructed prior to 1978, except any 0-bedroom dwelling or any dwelling located in multiple-unit buildings or projects reserved for the exclusive use of the elderly or persons with disabilities, unless a child six years of age or younger resides in or is expected to reside in that dwelling. "Target housing" does not include units in a hotel, motel, or other lodging, including condominiums that are rented for transient occupancy for 30 days or less.

Balance of Section as written.

Sec. 18-25. Orders.

Where any inspection of the property by a duly authorized city code official, fire inspector, law enforcement officer or health officer indicates that a violation of [the chapters listed below] exists, the inspecting officer or his delegate shall issue a written order notifying the party responsible of the existence of the violation and the measure required to correct or eliminate it as soon as possible.

Table Insert.  As written.

Where there is a violation which materially affects health and safety, the enforcement officer will also notify the affected occupants of the rental units of the existence of said violation. At the discretion of the agency, the order may require the violations to be corrected within thirty (30) sixty (60) days or less unless otherwise noted in this code or require that the premises be vacated and secured until the dwelling or dwelling unit meets the standards of this chapter. The latter requirement shall be based on a finding that the premises are a serious danger to the health, welfare and safety of the occupants of or the general public. Orders may further direct:

- through (5)  As written.

Sec. 18-72. Floors, interior walls and ceilings.

The interior of a structure and its equipment shall be maintained structurally sound and in a sanitary condition so as not to pose a threat to the health and safety of the occupants and to protect the occupants from the environment.

(a)  As written.

(b)  As written.

(c)  Lead-based paint with a lead content of more than five-tenths (0.5) per cent shall not be applied to any interior or exterior surface of a dwelling or dwelling unit, including fences and outbuildings at these locations. For the purposes of this ordinance, lead-based paint means the same as “lead-based paint” in Title 18, chapter 38 of the Vermont  Statutes.

Sec. 18-112. Paint.

(a)	Painted surfaces generally.

(1) In rental target housing, all windows, walls, floors, doors, or other surfaces, interior or exterior, of a dwelling shall be free from deteriorated painted surfaces equal to or greater than 1 square foot in the aggregate.  “Deteriorated painted surfaces” are those surfaces which are peeling, chipping, chalking, cracking, damaged or similarly deteriorated. “Deteriorated paint” means the same as the term is defined in Title 18, chapter 38 of the Vermont  Statutes.

(2) Owner(s) of rental target housing shall conduct a visual assessment of each unit annually and at tenant turnover for the presence of deteriorated painted surfaces, and will promptly and safely repair and/or stabilize all deteriorated surfaces, within 30 days, if more 1 square foot of interior room or 1 square foot of exterior wall surface is found or reported damaged.  If exterior deteriorated paint was found or reported after November 1, the owner shall have until the following May 31 to repair and/stabilize area(s), provided that access to surfaces and components with lead hazards and areas directly below the deteriorated surfaces is clearly restricted. A record of visual assessments and repair and/or stabilization shall be kept on the affidavit compliance statement of performance of essential maintenance practices (EMPs) required by subsection (h).

(3) Owners shall keep the outdoor areas of rental target housing free from visible paint chips.

(b)	Lead-based paint.

The presence of lead-based paint in and around dwellings is a substantial health hazard which necessitates that special safety activities be used when working in and around lead-based paint.  All paint shall be presumed to be lead-based paint (LBP) when present on all dwellings constructed prior to January 1, 1978 unless the paint was found to be not lead-based by a Vermont certified lead testing inspector who has issued a report to the owner of their findings. Property owner(s) wishing to be exempt from all LBP compliance activities under this ordinance must submit a copy of the certified inspectors’ written report showing the dwelling to be free of LBP to the Code Enforcement Office.

(c)	Lead safe work practices

- Interior lead safe work practices.  All activities to all rental target housing that disturb more than 1 square foot of painted interior surface(s) shall be done using Lead Safe Work Practices (LSWP) which take all reasonable precautions against the generation and spreading of lead dust, paint chips and debris.  Interior LSWP include, but are not limited to, the following:

  - limiting access of work area(s) to workers only;

  - protecting occupant belongings by covering them with 6 mil plastic sheeting or removing them from the work area(s);

  - segregating work area(s) from clean area(s) by hanging plastic sheeting in doorways and/or window areas;

  - covering the floor(s) of work area(s) with adequate amounts (extended at least 5 ft from work area) of 6 mil plastic sheeting to capture all dust, paint chips and debris;

  - using vacuums with high efficiency particulate air (HEPA) filters attached to scrapers; wetting surfaces with water prior to disturbing the surface(s) (do not dry scrape);

  - misting dust and debris with water prior to sweeping and cleaning (do not dry sweep);

  - cleaning shoes and clothing when leaving work area(s);

  - using personal protective equipment as needed, such as a HEPA respirator, gloves and coveralls.

Certification that interior lead safe work practices were used must be made by the person doing the work on a form provided by the Code Enforcement Office and kept on file with the owner of the property for one year from the completion of the activity.

- Exterior lead safe work practices.  All activities to rental target housing that disturb more than 1 square foot of painted exterior surface(s) shall be done using LSWP which take all reasonable precautions against the generation and spreading of lead dust, paint chips and debris.  Exterior LSWP include, but are not limited to the following:

  - limiting access of work area(s) to workers only;

  - attaching 6 mil plastic sheeting to dwelling and extend at least 10’ (if possible) or as far as to be adequate to capture all dust, paint chips and debris (plastic sheeting to be misted with water, rolled up and thrown away each night);

  - cover gardens, sand boxes and play areas with adequate amounts of 6 mil plastic sheeting;

(D) closing all windows and doors on the side being scraped;

(E) closing all windows and doors on neighboring properties within 10’ of work area(s);

(F) using vacuums with HEPA filters attached to scrapers;

(G) wetting surfaces with water prior to disturbing the surface(s) (do not dry scrape);

(H) cleaning shoes and clothing when leaving work area(s);

(I) using personal protective equipment as needed, such as a HEPA respirator, gloves and

coveralls.

(J) Ground cover surrounding rental target housing that have undergone disturbances of more than 1 sf on any exterior painted surface must be free from all visible paint chips, dust, or debris.

Certification that exterior lead safe work practices were used must be made by the person doing the work on a form provided by the Code Enforcement Office and kept on file with the owner of the property for one year from the completion of the activity.

(3) In non-rental target housing, no person shall disturb more than one square foot of lead-based paint by failing to use one of more of the following lead-safe work practices, unless specifically authorized by a permit issued by the Vermont Department of Health:

(A) Limiting access to interior and exterior work areas.

(B) Enclosing interior work areas with plastic sheathing or other effective lead dust barrier.

(C) Using protective clothing.

(D) Misting painted surfaces before disturbing paint.

(E) Wetting paint debris before sweeping to limit dust creation.

(F) Any other measure required by the Vermont Department of Health.

Notwithstanding the provisions of section 18-31 (a) and (b) of this ordinance, if a violation of this subsection is found, the inspector shall issue an order to cease and desist the prohibited practice, remove all visible paint chips and clean the affected area using the safe cleaning methods approved by the Vermont Department of Health.  A failure to comply with such an order is a violation the penalty for which shall be a fine of up to $500.

(d) Prohibited work practices.

(1) The following practices are not allowed for use on rental target housing:

(A)dry scraping;

(B)open flame burning;

(C)uncontained power washing;

(D)heat guns operated above 1,100 degrees Fahrenheit;

(E)uncontained sandblasting;

(F)power sanding (unless fitted with a HEPA filter);and

(G)chemical stripping using products containing methylene chloride.

Certification that prohibited work practices were not used must be made by the person doing the work on a form provided by the Code Enforcement Office and kept on file with the owner of the property.

(2) The following practices are not allowed to be used to remove lead-based paint on non-rental target housing:

(A) Open flame burning or torching.

(B) Use of heat guns operated above 1,100 degrees Fahrenheit.

(C) Dry scraping.

(D) Machine sanding or grinding.

(E) Uncontained hydro-blasting or high-pressure washing.

(F) Abrasive blasting or sandblasting without containment and high-efficiency particulate exhaust controls.

(G) Chemical stripping using methylene chloride products.

Notwithstanding the provisions of section 18-31 (a) and (b) of this ordinance, if a violation of this subsection is found, the inspector shall issue an order to cease and desist the prohibited practice, remove all visible paint chips and clean the affected area using the safe cleaning methods approved by the Vermont Department of Health.  A failure to comply with such an order is a violation the penalty for which shall be a fine of up to $500.

(e) Enforcement of lead safe work practices.  In addition to all the other enforcement powers authorized by this chapter, inspectors shall have the authority to issue a stop work order if unsafe or prohibited work practices are being performed on target housing.

(f) Lead safe cleaning practices.  All activities to all rental target housing that disturb more than 1 square foot of painted interior surface(s) shall be followed by a specialized cleaning that employs techniques effective in collecting lead dust, paint chips and debris.  These techniques shall include, but are not limited to; wet sweeping; using vacuums with HEPA filters; wet scrubbing and wiping of surfaces numerous times with disposable towels; using a multi-bucket system when mopping; and using lead specific or other effective detergents. Certification that lead safe cleaning practices were used must be made by the person doing the work on a form provided by the Code Enforcement Office and kept on file with the owner of the property for one year from the completion of the activity.

(g) Installation of vinyl or metal inserts. Owner(s) of rental target housing units shall install vinyl or metal inserts in all window wells in accordance with the requirements of 18 VSA § 1759. A window well is the portion of the exterior window sill between the interior window sill (or stool) and the frame of the storm window. If there is no storm window, the window well is the area that receives both the upper and lower window sashes when they are both lowered.

(h) Owner’s responsibilities.

(1) Posting.

(A) Owner(s) of rental target housing shall post in a prominent location, a poster that meets the requirements of 18 VSA § 1759 which states the importance of occupants reporting deteriorated paint and the information of whom to contact.

(B) Owner(s) of target housing shall post in a prominent location a notice that informs abutting neighbors that exterior work which is subject to the provisions of section 18-112 is being done on their dwelling.  The form of such notice will be provided by the Code Enforcement Office and use appropriate universal symbols to make the notice easily understandable.

(2) Educational pamphlet. Owner(s) or owner(s) representative of rental target housing shall provide the Environmental Protection Agency (EPA) pamphlet ‘Protect Your Family from Lead in Your Home’, or any subsequent or superseding pamphlet, to tenants upon occupying the rental unit and annually thereafter.

(3) Certifications.  All work on rental target housing performed to comply with the requirements of this section must be certified on a form provided by the Code Enforcement Office that the required work was performed using lead safe work practices and lead safe cleaning practices and that the work was done or supervised by a person who has been certified by the state department of health as having successfully completed the essential maintenance practices course.  Owner(s) shall obtain and keep such certifications and provide a copy to the Code Enforcement Office upon request.

(4) Specialized cleaning at tenant turnover. Owner(s) of  rental target housing shall perform a specialized cleaning of all horizontal interior surfaces, except ceilings, at tenant turnover as set forth in subsection (f). Certification that specialized cleaning was done must be made by the person doing the work and kept on file with the owner of the property.

(5) Annual cleaning of common areas.   Owner(s) of rental target housing shall annually perform a specialize cleaning of all horizontal interior surfaces, except ceilings, in the common areas of the rental property accessible to tenants.

(6) Vermont compliance statements. Owner(s) of pre-1978 rental housing units rental target housing shall comply with the compliance statement requirements of 18 VSA § 1759 (b) and shall provide a copy of the current statement to the Code Enforcement Office as proof of compliance upon request.

(7) Disclosure of known lead based paint activities. Owner(s) of rental target housing shall disclose to tenants, records of all known lead based paint activities. A “lead based paint activity” means an inspection conducted by a lead inspector and/or risk assessment conducted by a lead risk assessor  and/or lead paint hazard reduction activity, as “inspection” is defined in 17 V.S.A. § 1751 (b) (10), “lead inspector” is defined in 17 V.S.A. § 1751 (b) (17), and “risk assessment” is defined in 17 V.S.A. § 1751 (b) (24), and as “lead paint hazard” is a “lead hazard”, as defined in 17 V.S.A. § 1751 (b) (16), created by “lead based paint” as that is defined in “17 V.S.A. § 1751 (b) (12). Owner(s) of rental target housing shall disclose all known lead based paint activities to perspective buyers.  Buyers of the property shall

keep records of all such known lead based paint activities. Owner(s) of pre-1978 rental properties undergoing activities that disturb more than 1 sf of painted surface(s) shall provide to the occupant(s) the Environmental Protection Agency (EPA) pamphlet ‘Protect Your Family from Lead in Your Home’, or subsequent or superceding pamphlet, and a description of the type of work that will take place, expected work dates and who to contact with questions about the work, at least 7 days prior to the commencement of work.

7

HOUSING -

Minimum Housing Amendments related to Lead Paint

(i) Contractor’s obligations. In addition to complying with the Pre-Renovation Rule or any subsequent superseding rule, using lead safe work practices, lead safe cleaning practices and not using prohibited work

practices, contractors that disturb more than 1 sf of painted surface(s) in pre-1978 dwellings shall provide to the owner(s) the Environmental Protection Agency (EPA) pamphlet ‘Protect Your Family from Lead in Your Home’, or subsequent or superceding pamphlet, and a description of the type of work that will take place, expected work dates and who to contact with questions about the work, at least 7 days prior to the commencement of work, except in emergency circumstances, in accordance with the Pre-Renovation Rule.

*	Material stricken out deleted.

**	Material underlined added.

lb/emb/c: Ordinances 2008/Housing – Min. Housing related to Lead Paint, Sec. 18-2, 18-25, 18-72, 18-112

2/19/09