Burlington Comprehensive Development Ordinance

PROPOSED ZA-09-07 Minimum Side Setback Clarification (Residential Districts)

As recommended by the Planning Commission on January 13, 2009

### Changes shown (underline to be added, strike-out to be deleted) are proposed changes to the Burlington Comprehensive Development Ordinance.

### Table 4.4.5-3: Residential District Dimensional Standards

| Table 4.4.5-3: Residential District Dimensional Standards |
| --- |
| Zoning District | Max. Lot Coverage1 | Setbacks1, 3, 4 | Max. Height1 |
|  |  | Front2 | Side3 | Rear | Waterfront |  |
| RL; WRL | 35% | Min/Max: Ave. of 2 adjacent lots on both sides +/- 5-feet | Min: 10% of lot width or but in no event less than 5’ Max required: 20-feet | Min: 25% of lot depth but in no event less than 20’ Max required: 75-feet | Min: 75’ from the ordinary high water mark of Lake Champlain and the Winooski River | 35-feet |
| RM | 40% | Min/Max: Ave of 2 adjacent lots on both sides +/- 5-feet | Min: 10% of lot width or but in no event less than 5’ Max required: 20-feet | Min: 25% of lot depth but in no event less than 20’ Max required: 75-feet | NA | 35-feet |
| WRM | 60% | Min/Max: Ave of 2 adjacent lots on both sides +/- 5-feet | Min: 10% of lot width or but in no event less than 5’ Max required: 20-feet | Min: 25% of lot depth but in no event less than 20’ Max required: 75-feet | Min: 75’ from the ordinary high water mark of Lake Champlain and the Winooski River | 35-feet (60-feet under Sec. 4.4.5(d)2A) |
| RH | 80% | Min/Max: Ave of 2 adjacent lots on both sides +/- 5-feet | Min: 10% of lot width or but in no event less than 5’ Max required: 20-feet | Min: 25% of lot depth but in no event less than 20’ Max required: 75-feet | NA | 35-feet |
| An additional ten per cent (10%) lot coverage may be permitted for accessory residential features per (d)3A below. Measurement of and exceptions to coverage, setback, and height standards are found in Art 5. Average front yard setback of the principal structures on the 2 adjacent lots within the same block having the same street frontage. See Sec. 5.2.4. In no event shall the side yard setback be required to exceed 20-feet, or the rear-yard setback be required to exceed 75-feet. Additional setbacks from the lakeshore and other water features may be applicable per the requirements of the Sec 4.5.4 Riparian and Littoral Conservation Overlay Zone |